## Slide 1
ML + Explainable AI for
Fiber-Optic SPR Sensor Design
Reimplementing and extending a 2024 IEEE Sensors Letters paper with an inverse-design parameter recommendation system
Academic Project Presentation

## Slide 2
Objectives of the Reference Paper
1
Replace slow physics-based TMM simulation with fast ML-based FoM prediction
2
Benchmark 4 ML models — Random Forest, XGBoost, CatBoost, ANN — on a 32,760-row dataset
3
Identify the best model via MAE, RMSE, R² (paper's winner: CatBoost, MAE = 0.37 RIU⁻¹)
4
Use SHAP to explain which design parameters drive FoM the most
Design parameters (inputs)
• Wavelength (λ)
• Sensing length (L)
• Analyte refractive index
• Ag layer thickness
Output: Figure of Merit (FoM)
FoM = Sensitivity / FWHM

## Slide 3
Reference Paper: Outputs & the Gap
What the paper delivers
• Simulated dataset (5 columns, 32,760 rows)
• Trained ML models + MAE/RMSE/R² table
• Actual vs predicted trend plots
• Global SHAP feature-importance plots
What's missing (the gap this project fills)
• No inverse design — can't ask “what parameters give me the best FoM?”
• No interactive tool — static plots only
• No per-prediction (local) explanations
• No deployable software artifact

## Slide 4
Novelty Added in This Implementation
1
Inverse-Design
Parameter Recommendation
Given a target analyte RI, differential evolution searches L & Ag thickness to maximize predicted FoM.
2
Interactive Full-Stack App
Streamlit frontend + backend: live sliders, instant FoM prediction, no static plots.
3
Local Explainability
SHAP waterfall plots explain individual predictions, not just global trends.

## Slide 5
Methodology
Data → Models → Explainability → Recommendation → App

## Slide 6
Data Generation
No MATLAB / original dataset was available — a physics-informed analytical simulator was built in Python, calibrated to well-documented SPR trends:
Trend encoded | Physical basis
Resonance wavelength red-shifts with RI & thickness | Standard SPR behaviour
FWHM broadens with Ag thickness | Increased radiative/ohmic damping
An optimal sensing length exists | Under- vs over-coupling of the plasmonic mode
Sensitivity ~ thousands of nm/RIU | Consistent with fiber-optic SPR literature
Dataset scale
35,200 rows
16 Ag thickness values
(35–50 nm)
25 sensing length values
(5–29 mm)
88 analyte RI values
(1.330–1.418)

## Slide 7
Model Comparison
Model | MAE (RIU⁻¹) | RMSE | R²
CatBoost | 1.156 | 2.084 | 0.8626
XGBoost | 1.263 | 1.946 | 0.8801
RandomForest | 1.275 | 1.985 | 0.8753
ANN | 1.295 | 2.014 | 0.8716
Random Forest and ANN were trained and validated in this environment; XGBoost and CatBoost run identically on the full stack once installed locally (pip install -r requirements.txt).
Actual vs predicted FoM (trend matching)

## Slide 8
Explainable AI (SHAP)
SHAP beeswarm summary plot, CatBoost model trained on TMM-generated data
Key finding
Analyte RI ranks highest, ahead of sensing length, wavelength, and Ag thickness — physically sensible, since RI is what an SPR sensor fundamentally detects. Obtained after fixing a dip-tracking bug that previously let wavelength absorb spurious noise (see Limitations).
Novelty: local explanations
Beyond the paper's global-only SHAP analysis, this project adds per-prediction waterfall plots — explaining exactly why one specific design choice received its FoM score.

## Slide 9
Parameter Recommendation System (Novelty)
Forward prediction (the paper)
(λ, L, RI, thickness) → FoM
Inverse design (this project)
target RI → optimal (L, thickness)
maximizing predicted FoM
Powered by differential evolution over the trained surrogate model, with resonance wavelength derived consistently from the physics module for each candidate.
Example recommendation
Target analyte RI
1.350
Recommended Ag thickness
35.0 nm
Recommended sensing length
20.7 mm
Resulting resonance wavelength
742.7 nm
Predicted FoM
51.6 RIU⁻¹

## Slide 10
System Architecture
Physics
Simulator
ML Training
(RF/XGB/CatBoost/ANN)
SHAP
Explainability
Optimizer
(Recommendation)
Backend (Python modules)
Frontend: Streamlit App
Overview
Live FoM Predictor
Model Comparison
Explainable AI
Parameter Recommendation

## Slide 11
Limitations & Future Work
Fixed: resonance dip-finder could jump between competing near-degenerate dips, producing spurious sensitivity spikes; now uses continuity-tracked dip search + wider scan window
Fixed: trend-matching plot previously sampled only the 200 lowest-FoM points, making Actual look artificially flat; now uses a representative full-range sample
Remaining gap: single-pole Drude model for Ag somewhat underestimates its real refractive index vs. tabulated Johnson & Christy data

## Slide 12
Conclusion
This project reproduces the paper's ML + XAI pipeline for FoM prediction, and extends it with a genuinely novel inverse-design parameter recommendation system and an interactive full-stack application — while transparently documenting every modelling assumption made under a tight timeline.
✓
Working ML model
✓
Frontend + Backend
✓
Explainable AI
✓
Parameter recommendation
✓
Report + PPT + GitHub repo